## Slide 1
DAQ 2025s
MechPulse
Multi-Sensor Machine Health Monitor
Team 22 : GK Fastfood
Kawin KAEWPARADAI · Kantee LAIBUDDEE
KY-002 · KY-028 · KY-037 · KY-031 → ESP32 → MQTT → Node-RED → MySQL → FastAPI → React

## Slide 2
2.1 Overview & Motivation
The Problem
Rotating machinery (motors, fans) fails without warning.
Unexpected downtime causes costly damage and production loss.
Manual inspection is slow and misses early-stage faults.
No single signal is sufficient — combined sensing gives higher accuracy.
MechPulse Solution
4 KY sensors on ESP32 sample every ~5 seconds.
Node-RED routes data via MQTT into a shared MySQL DB.
FastAPI computes a 0–100 Health Score and z-score anomalies.
React dashboard gives real-time visibility: time-series, heatmap, alerts, daily reports.
MechPulse · Team 22 : GK Fastfood · DAQ 2025s

## Slide 3
2.2 Overall Architecture
Sensors
KY-002/028
037/031
Physical
ESP32 MCU
Edge device
~5s cycle
Edge
MQTTX
Pub/Sub
broker
Pub/Sub
Node-RED
Parse &
insert
Route &
Store
MySQL
sensor_data
iot.cpe.ku
Storage
FastAPI
Analytics
API
Analytics
React
Dashboard
UI
UI
Each layer has a single responsibility — any component can be swapped independently.
MechPulse · Team 22 : GK Fastfood · DAQ 2025s

## Slide 4
2.3 Primary Data Source — KY Sensor Suite
KY-002 · Vibration
Analog vibration amplitude. Measures intensity & frequency patterns of rotating parts.
KY-028 · Temperature
Digital surface temperature. Detects overheating above reference threshold (45 °C).
KY-037 · Sound Level
Analog sound level. Captures grinding, rattling and abnormal acoustic signatures.
KY-031 · Knock/Impact
Digital tap detection. Flags sudden mechanical shocks or irregular impacts.
Collection Method: ESP32 reads all 4 sensors on a fixed ~5 s cadence → assembles JSON payload → publishes to MQTT topic mechpulse/<machine_id>/reading
MechPulse · Team 22 : GK Fastfood · DAQ 2025s

## Slide 5
2.3 Secondary Data Sources
Manufacturer Specifications
Reference operating values stored as REF_* environment variables:
Variable | Value | Meaning
REF_TEMP_C | 45 | Max normal temp (°C)
REF_VIB_COUNT | 5 | Max vibration count
REF_SOUND_AVG | 870 | Normal sound avg
REF_SOUND_VAR | 60 | Normal sound variance
Historical Baseline Phase
The first N rows where phase = "baseline" define calibration statistics:
Mean (μ) and Standard Deviation (σ)
Used by the /api/analytics/anomalies endpoint to compute per-column z-scores.
Z-score formula:
z = (x − μ) / σ
Severity levels: info → warning → critical
Cross-validation: severity upgraded when ≥ 2 sensors fire at the same timestamp.
MechPulse · Team 22 : GK Fastfood · DAQ 2025s

## Slide 6
2.4 Database Schema — sensor_data
MySQL — iot.cpe.ku.ac.th/pma
Table: sensor_data
Index: idx_sensor_ts (timestamp)
Column | Type | Description
id | INT AUTO_INCREMENT PK | Unique row identifier
timestamp | DATETIME NOT NULL | Indexed — time of reading
phase | VARCHAR(20) | baseline / warmup / running / cooldown
cycle | INT | Monotonic counter within phase
vib_count | INT | Vibration event count (KY-002)
knock_count | INT | Knock/impact count (KY-031)
sound_avg | INT | Average sound level (KY-037)
sound_var | INT | Sound variance (KY-037)
temperature_c | FLOAT NULL | Surface temperature °C (KY-028)
MechPulse · Team 22 : GK Fastfood · DAQ 2025s

## Slide 7
2.5 Data Sharing API — FastAPI + Node-RED
FastAPI Endpoints (OpenAPI docs at /docs)
Method | Path | Description
GET | /api/health | Liveness + DB connection check + row count
GET | /api/schema | Columns in the sensor_data table
GET | /api/sensors/latest | Most recent N rows
GET | /api/sensors/timeseries | Single-metric time-series (phase filter)
POST | /api/sensors/ingest | Insert a new row (MQTT bridge / testing)
GET | /api/analytics/stats | Count / mean / std / quantiles per column
GET | /api/analytics/correlation | Pearson / Spearman / Kendall matrix
GET | /api/analytics/health-score | Composite 0–100 health score + components
GET | /api/analytics/anomalies | Z-score anomalies: info / warning / critical
GET | /api/analytics/daily-summary | Peak vib, avg sound, impact count per day
Node-RED also exposes HTTP JSON endpoints: GET /api/sensor and GET /api/weather (both with optional ?limit=N)
MechPulse · Team 22 : GK Fastfood · DAQ 2025s

## Slide 8
2.6 Data Visualization — React Dashboard
Dashboard
Live health score (0-100)
Recent time-series charts
Anomaly alert panel
Latest sensor stats
Analytics
Pearson/Spearman/Kendall heatmap
Descriptive stats table
Column correlation explorer
Filter by phase
Architecture
Interactive SVG pipeline diagram
Layer descriptions
Component responsibilities
Stack documentation
Reports
Daily summary table
Peak vibration per day
Anomaly log (info/warn/crit)
Impact & sound trends
Stack: React + Vite + Tailwind CSS + Recharts + React Router · API polling every 10 s

## Slide 9
2.7 Demonstration of Key Features
Machine Health Score (0–100)
Composite score from 4 weighted penalties: vibration excess, knock excess, sound deviation, temperature breach.
Score 100 = perfectly healthy. Drops when any metric exceeds its REF_* reference threshold.
92
Z-Score Anomaly Detection
Per-column z-scores vs baseline (mean + std). Severity: Info (z>2), Warning (z>3), Critical (z>4).
Cross-sensor validation: severity upgraded when ≥2 sensors fire at the same timestamp — reduces false positives.
Info
Warn
Crit
Correlation Heatmap — 3 Methods
Pearson, Spearman, and Kendall correlation matrices computed on demand.
Constant columns are auto-ignored. Renders as an interactive color heatmap in the Analytics page.
MechPulse · Team 22 : GK Fastfood · DAQ 2025s

## Slide 10
Thank You!
MechPulse — Multi-Sensor Machine Health Monitor
4 KY sensors · ESP32 · MQTT · Node-RED
MySQL (iot.cpe.ku.ac.th) · FastAPI · React + Recharts
Health Score · Z-Score Anomalies · Correlation Matrix
Source Code: GitHub (Tag: v1.0) · DB: sensor_data table
Team 22 : GK Fastfood | Kawin KAEWPARADAI · Kantee LAIBUDDEE | DAQ 2025s — Due April 21, 2026